| Firmware Version: | v1.03.04 |
| --- | --- |
| Prom Code Version: |  |
| Published Date: | 2015/9/1 |

Content:

New Features:	2

Problems Fixed:	2

Known Issues:	3

Related Documentation:	3

Upgrading Instructions:	3

Revision History and System Requirement:

| Firmware Version | Date | Model | Hardware Version |
| --- | --- | --- | --- |
| v1.03.04 | 2015/9/1 | DCS-850L | A1 |
| v1.02.09 | 2015/6/16 | DCS-850L | A1 |
| v1.01.06 | 2015/3/16 | DCS-850L | A1 |
| v1.00b7 | 2014/10/30 | DCS-850L | A1 |

# New Features:

| Firmware Version | New Features |
| --- | --- |
| V1.03.04 | Update mydlink agent to v2.0.19-b54 Add the denoise mechanism to reduce the background noise Add the login check mechanism to solve Brute Force Attack issue |
| v1.02.09 | Update mydlink Agent to v2.0.19-b35 Remove Bonjour _http service, and add Bonjour _dcamera service Support CGI command of auto-pan stop |
| v1.01.06 | Upgrade mydlink agent to v2.0.18-b61 Remove SSL, change to support TLS. |
| v1.00b7 | 1st version |

# Problems Fixed:

| Firmware Version | Problems Fixed |
| --- | --- |
| v1.02.09 | Fixed HTTPS issue that cause Pan/Tilt and Day/Night control not work from portal/app Modify Time Zone Table list to support some existing time zones changes. Fixed when IP Cam connects to wireless router and its Direct Mode is also activated simultaneously, the wireless devices can discover other IP cameras (connect to wireless router) through the AP mode connection. Fixed IP Cam can not connect to a Wireless Network with a Hidden SSID. Fixed CGI /reset.cgi reboot command not work issue |

# Known Issues:

| Firmware Version | Known Issues |
| --- | --- |

# Related Documentation:

N/A

# Upgrading Instructions:

Follow the steps below to upgrade the firmware:

1. Download the latest firmware file from the D-Link website. The file is in .bin file format.

For Windows:

Step 1

In the Control Panel, click Network and Internet.

Step 2

Click View network computers and devices.

Step 3

Make a note of the camera’s IP address.

Step 4

Open a web browser and enter “http://IP_Address/eng/admin/tools_firmware.cgi” in the address bar (where IP_Address is the IP address you made a note of in Step 3).

Step 5

If you do not already have the firmware file to use, follow the instructions on this page to download the latest file from the D-Link Support Page. Then click Browse… and locate the file. Finally, click the Upload button.

For Mac:

Step 1

Open Safari, and click Bonjour.

Step 2

Select the device you want to perform the firmware upgrade on.

Step 3

Add “/eng/admin/tools_firmware.cgi” to the address currently in the address bar and press Enter.

Step 4

If you do not already have the firmware file to use, follow the instructions on this page to download the latest file from the D-Link Support Page. Then click Browse… and locate the file. Finally, click the Upload button.